## Slide 1: Basic Sequential Circuits
A combinational circuit produces output solely depending on the current input.
But a sequential circuit “remembers” its previous state.
Its output depends on present inputs and previous state.
Examples:
  Latches
  Registers
  Memory
  parallel to serial / serial to parallel converters
  Counters

## Slide 2: Latch vs Registers
Latch: Level sensitive device
  Positive Latches and Negative latches
  Can be realized using multiplexers
Register: edge triggered storage element
  Can be implemented using latches
  Cascade a negative latch with a positive latch to obtain a positive edge triggered register
Flip flop: bi-stable component formed by the cross coupling of gates.

## Slide 3: Sequential Switching Networks
Sequential logic forms basis for building
"memory" into circuits.
Sequential logic is characterized by the
presence of feedback paths.
Combinational
Logic
Delay = D
x1
x2
x3
x4
z1
z2
z3
z4
z3 = F(x1, ... ,x4,z3,z4)
z3(t+D) = F(x1(t), ... ,x4(t),z3(t),z4(t))
Observations:
z3 and z4 appear as both
inputs and outputs.
The “state” of variable z3 (or z4) at
time t+D depends on its value at
time t, i.e. z3(t+D) = F(z3(t)),
hence, circuit has memory.
z3(t) and z4(t) are called
state variables .
Sequential Circuit

## Slide 4: Simple Sequential Circuits
Cascaded Inverters: Static Memory Cell
"0"
"1"
Delay=D
x(t)
z(t)
D
D
t
x
z
Assuming D > 0
z(t+D) = x(t) z(t)
if x(t) = 0 then z(t)=1 (stable state)
if x(t) = 1 then z(t+D) = z(t)
Another Example
Observe that
NAND gate with one input asserted
acts as an inverter with respect to
other input
When x=1, equaivalent circuit
z(t)
Timing Waveform:

## Slide 5: Cross-Coupled NOR Gates
Observation
NOR gate with one input=0, acts as an
inverter with respect to other input.
0
x
X
x(t)
z(t)
x=1 --> z=0
x=0 --> z=1
Problem: how can we insert x in the loop?
Simple-Latch: two-inverter loop
q
Q
R
S
Equivalent NOR circuit with two control
inputs (R and S) to break or close the loop
R: Reset input (R=1 --> Q=0)
S: Set input (S=1 --> Q=1)
q
Q
R
S
Alternative
representation

## Slide 6: The RS Latch
q=0
Q=1
R=0
S=0
if R=S=0 then Q(t+D)=Q(t) (memory element)
q=1
Q=0
R=0
S=0
q=0
Q=0
R=1
S=1
if R=S=1 then q = Q = 0, which violates the inverter rule (q = 0, Q = 1)
if R and S chnage from 1-to-0 at precisely same moment, then RS latch
will oscillate (provided the NOR gate delays are perfectly matched)
q=0-->1-->0-->1--
Q=0-->1-->0-->1--
R=1-->0
S=1-->0
0-->1-->0-->1
0-->1-->0-->1

## Slide 7: State Behavior of RS Latch
Truth Table Summary
of R-S Latch Behavior
The response and transient behavior of the RS latch can be described
using a state-diagram:
1- Nodes represent the unique states
of the circuit
2- Arcs indicate state-transition under
particular input combinations
(arc labels).
Because of the resulting unstable behavior
the combination R=S=1 is called the forbidden
input for the RS latch.
state 0
state 3
state 1
state 2

## Slide 8: The D-Latch
enabled when C=1
D
C
Clk
Enable
Q
q
if C=1 then Q=D
if C=0 then Q(t+D)=Q(t)
if C=0, then R=S=0
and Q(t+D)=Q(t)
If C=1 and D=0 then
R=1, S=0, and Q=0
if C=1 and D=1 then
R=0, S=1, and Q=1
Realization using an RS latch
Note that input R=S=1
can not occur
R
S
Q
q
q
D
C
RS
Latch

## Slide 9: Setup and Hold Times
Clock:
Periodic Event, causes state of memory
element to change.
There is a timing "window" around the
clocking event during which the input
must remain stable and unchanged
in order to be recognized
Setup Time (Tsu):
Minimum time before the clocking event by
which the input must be stable
Hold Time (Th)
Minimum time after the clocking event during
which the input must remain stable
Primitive Memory Elements:
Latches: Continuously sample their inputs. Any change in the level of the inputs
is propagated through to the outputs (level sensitive).
Flip-Flops: Outputs change only with respect to the clock, normally the rising edge
or the falling edges of the clock.

## Slide 10: Level Sensitive Latches
Timing Diagram:
Set
Reset
RS latch with active-low inputs and active-low Enable
Truth Table
\enb S R Q+
1 x x Q
0 0 0 Q
0 0 1 0
0 1 0 1
0 1 1 Unstable

## Slide 11: Flip-Flops and Latches
Bubble here for negative
edge triggered device
Timing Diagram:
Behavior is the same unless input changes
occur while the clock is high
Edge triggered devices sample inputs on the rising
or falling edge of the Clock or the Enable.
Transparent latches sample inputs as long as the
clock is asserted -
output changes with input (after certain delay).

## Slide 12: Flip-Flops vs. Latches
Input/Output Behavior of Latches and Flipflops
Type When Inputs are Sampled When Outputs are Valid
unclocked always propagation delay from
latch input change
level clock high propagation delay from
sensitive (Tsu, Th around input change
latch falling clock edge)
positive edge clock lo-to-hi transition propagation delay from
flipflop (Tsu, Th around rising edge of clock
rising clock edge)
negative edge clock hi-to-lo transition propagation delay from
flipflop (Tsu, Th around falling edge of clock
falling clock edge)
master/slave clock hi-to-lo transition propagation delay from
flipflop (Tsu, Th around falling edge of clock
falling clock edge)

## Slide 13: Flip-Flops: Typical Timing Specifications
Positive
Edge Triggered
D Flipflop
• Setup time
• Hold time
• Minimum clock width
• Propagation delays
(low to high, high to low,
max and typical)
All measurements are made from the clocking event
that is, the rising edge of the clock

## Slide 14: Latches: Typical Timing Specifications
Transparent
Latch
• Setup time
• Hold time
• Minimum Clock Width
• Propagation Delays:
high to low, low to high,
maximum, typical
data to output
clock to output
Measurements from falling clock edge
or rising or falling data edge

## Slide 15: Designing Latches
RS Latch
Truth Table:
Next State = F(S, R, Current State)
Derived K-Map:
Characteristic Equation:
q(t+D)=s(t)+R(t)q(t)
or
q+=s + Rq
q
Q
R
S
q
q
R
S
Compare to previous NOR implementation

## Slide 16: The JK Latch
The JK latch eliminates the forbidden state of the RS latch
Basic principle:
use output feedback to guarantee
that R=S=1 never occurs
J=K=1 yields toggle (q+ = Q)
Characteristic Equation:
Q+ = Q K + Q J
J
K
D
C
Q
enb
D-Latch

## Slide 17: JK Latches
q SR SR SR SR
00 01 10 11
0 0 0 1 x
1 1 0 1 x
Q Q 0 1 x
PS
NS (q+, Q+)
Simplified State-Tables
q JK JK JK JK
00 01 10 11
0 0 0 1 1
1 1 0 1 0
Q Q 0 1 Q
PS
NS (q+, Q+)
JK=01 , 11
JK=10 , 11
JK=00 , 10
JK=00, 01
Q=1
Q=0
J K Q+
0 0 Q
0 1 0
1 0 1
1 1 Q

## Slide 18: From JK Latch to JK Flip-Flop
JK Latch: Race Condition
Set
Reset
Toggle
Race Condition
Ideally, the Latch should toggle only once when JK=11.
Because of latch transparency, race conditions cause continuous toggrling.
Toggle Correctness: Single State change per clocking event
Solution: Master-Slave Flipflop

## Slide 19: Master-Slave JK Flip-Flop
Correct Toggle
Operation
Master Stage
Slave Stage
Sample inputs while clock high
Sample inputs while clock low
Break feedback path, by dividing operation in two time periods
(clock-high and clock-low)

## Slide 20: The Toggle (T) Flip Flop
State table
T Q Q+
0 0 0
0 1 1
1 0 1
1 1 0
T
Q
C
T
flipflop
JK
flipflop
T
J
K
C
Q
T-FF can be realized using a JK-FF
Verification: J=K=T
T Q+
0 Q
1 Q
or
T J K Q+
0 0 0 q
1 1 1 Q
q+ = tQ+Tq
D
flipflop
T
D
C
Q
T-FF can be realized using a D-FF

## Slide 21: Edge-Triggered Flip Flops
Characteristic equation
Q+ = D
Negative edge-triggered D flipflop
Flipflop state changes right after the falling edge of the clock
4-5 gate delays (longer than latches)
Setup and Hold times are necessary for correct operation
Example:
D
Clk
Q

## Slide 22: Edge-Triggered D Flip Flops
Step-by-step analysis
When clock goes from
high-to-low data is latched
When clock is low data is held

## Slide 23: Positive and Negative Edge Triggered Flip Flops
Positive Edge Triggered
Inputs sampled on rising edge
Outputs change after rising edge
Negative Edge Triggered
Inputs sampled on falling edge
Outputs change after falling edge
Timing Diagram

## Slide 24: Comparison
R-S Clocked Latch:
used as storage element in narrow width clocked systems
its use is not recommended!
however, fundamental building block of other flipflop types
J-K Flipflop:
versatile building block can be used to implement D and T FFs
usually requires least amount of logic to implement ƒ(In,Q,Q+)
but has two inputs with increased wiring complexity
because of 1's catching, never use master/slave J-K FFs
Use edge-triggered varieties
D Flipflop:
minimizes wires, much preferred in VLSI technologies
simplest design technique
best choice for storage registers
T Flipflops:
don't really exist, constructed from J-K FFs
usually best choice for implementing counters

## Slide 25: Flip Flop Excitation Tables
Useful Design Tool:
For each state-transition, the excitation table lists the required input combination(s)
D Q+
0 0
1 1
D
Q
C
D
flipflop
q+ = d
T
Q
C
T
flipflop
q+ = tQ+Tq
Q Q+ D
0 0 0
0 1 1
1 0 0
1 1 1
Excitation Table
Q Q+ T
0 0 0
0 1 1
1 0 1
1 1 0
1. D FlipFlop
2. T FlipFlop
Transition Table
T Q+
0 q
1 Q
Excitation Table
Transition Table

## Slide 26: Flip Flop Excitation Tables
q+ = s + Rq
Q Q+ R S
0 0 X 0
0 1 0 1
1 0 1 0
1 1 0 X
1. SR FlipFlop
R
Q
Clk
SR
flipflop
S
Transition Table
Excitation Table
R S Q+
0 0 Q
0 1 1
1 0 0
1 1 forbid
q+ = jQ + Kq
Q Q+ J K
0 0 0 X
0 1 1 X
1 0 X 1
1 1 X 0
1. JK FlipFlop
J
Q
Clk
JK
flipflop
K
Transition Table
Excitation Table
R S Q+
0 0 q
0 1 1
1 0 0
1 1 Q
Q=0
Q=1
JK= 10, 11
JK= 01, 11
JK=00,01
JK=00,10
Q=0
Q=1
RS= 01
RS=10
RS=00,10
RS=00,01

## Slide 27: Conversion Between Flip Flop Types
Procedure uses excitation tables
Method: to realize a type A flipflop using a type B flipflop:
1. Start with the K-map or state-table for the A-flipflop.
2. Express B-flipflop inputs as a function of the inputs and present state of
A-flipflop such that the required state transitions of A-flipflop are reallized.
x
y
Q
Type B
x
y
Q
g
h
CL
CL
Type A
1. Find Q+ = f(g,h,Q) for type A (using type A state-table)
2. Compute x = f1(g,h,Q) and y=f2(g,h,Q) to realize Q+.

## Slide 28: Conversion Between Flip Flop Types
Example: Use JK-FF to realize D-FF
1) Start transition table for D-FF
2) Create K-maps to express J and K as functions of inputs (D, Q)
3) Fill in K-maps with appropriate values for J and K
to cause the same state transition as in the D-FF transition table
State-Table
D Q Q+ J K
0 0 0 0 X
0 1 0 X 1
1 0 1 1 X
1 1 1 X 0
e.g.
when D=Q=0, then Q+= 0
the same transition Q-->Q+
is realize with J=0, K=X

## Slide 29: Conversion Between Flip Flops
Another Example: Implement JK-FF using a D-FF
J K Q Q+ D T
0 0 0 0 0 0
0 0 1 1 1 0
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 1 1 1
1 0 1 1 1 0
1 1 0 1 1 1
1 1 1 0 0 1
0
0
1
1
0
1
1
0
00
01
11
10
J
K
JK
Q
0
1
t= jQ + kq
0
0
1
1
1
0
0
1
00
01
11
10
J
K
JK
Q
0
1
d= jQ + Kq
J
K
D
C
Q
Clk
DFF
J
K
T
C
Q
Clk
T-FF

## Slide 30: Asynchronous Inputs
PRESET and CLEAR:
asynchronous, level-sensitive inputs
used to initialize a flipflop.
D
C
S
R
Q
Q
0
1
0
1
0
1
Q
Clk
SET
CLR
T
Clk
T
Q
CLEAR
PRESET
PRESET, CLEAR: active low inputs
PRESET = 0 --> Q = 1
CLEAR = 0 --> Q = 0

## Slide 31: Proper Cascading of Flip flops
Correct Operation,
assuming positive
edge triggered FF
FF0
FF1
Serial connection of positive edge-triggered flipflops
1. on rising edge of CLK, FF1 reads Q0, and FF0 reads IN
2. during clock period FF1 performs Q1 <-- Q0, and FF0 performs Q0 <-- IN
Shift-register